## Slide 1: Signed Integer Representations

## Slide 2: Signed Integer Representations
Positional number arithmetic
  Addition, subtraction, multiplication, and division is done by column in base 10.
    Example:
28341
-18754
9587

## Slide 3: Signed Integer Representations
Positional number arithmetic
  Addition, subtraction, multiplication, and division is done by column in base 10.
    Example:
28341
-18754
9587
This is a “signed magnitude” representation of numbers. Requires complex algorithms to “borrow” from columns.

## Slide 4: Signed Integer Representations
Positional number arithmetic
  The same general process can be followed in binary.
    Example:
101101001
-001011000
100010001

## Slide 5: Signed Integer Representations
Positional number arithmetic
  The same general process can be followed in binary.
    Example:
101101001
-001011000
100010001
Still need to “borrow” from columns.

## Slide 6: Signed Integer Representations
Positional number arithmetic
  Negative number representations—all use fixed width fields (i.e., a 16- or 32-bit integer)
    Simple binary—assumes all numbers are positive
      6610 = 010000102
      19410 = 110000102
Problem: Can’t represent negative numbers.

## Slide 7: Signed Integer Representations
Positional number arithmetic
  Negative number representations—all use fixed width fields (i.e., a 16- or 32-bit integer)
    Signed magnitude—use most significant bit to represent the sign. 0 is positive, 1 is negative.
      6610 = 010000102
      -6610 = 110000102
Problem: requires separate addition and subtraction algorithms in CPU hardware. Also, 10000000 is negative zero!

## Slide 8: Signed Integer Representations
Positional number arithmetic
  Negative number representations—all use fixed width fields (i.e., a 16- or 32-bit integer)
    Binary coded decimal—represent each base 10 digit in 4 bits. Use strings of 4 bits (nibbles) to encode a number.
      12310 = 0000 0001 0010 0011
      -12310 = 1010 0001 0010 0011
Problems: takes more memory; difficult to do arithmetic (forcing a base 2 computer to do base 10 arithmetic)

## Slide 9: Signed Integer Representations
Positional number arithmetic
  Negative number representations—all use fixed width fields (i.e., a 16- or 32-bit integer)
    Two’s complement—an encoding such that the fixed-width bit patterns are divided up into a range of [-2n-1…2n-1-1] for n-bits, and subtraction is merely addition of a negative number.

## Slide 10: Signed Integer Representations
Constructing a negative number in two’s complement
  Form the simple binary (positive) representation of the number.
  Flip all the bits (exchange 0’s for 1’s and 1’s for 0’s).
  Add 1 to the resulting number.

## Slide 11: Signed Integer Representations
Constructing a negative number in two’s complement
  Form the simple binary (positive) representation of the number.
  Flip all the bits (exchange 0’s for 1’s and 1’s for 0’s)
  Add 1 to the resulting number.
Example: Construct -24856 in 16-bit two’s complement.

## Slide 12: Signed Integer Representations
Constructing a negative number in two’s complement
  Form the simple binary (positive) representation of the number.
  Flip all the bits (exchange 0’s for 1’s and 1’s for 0’s)
  Add 1 to the resulting number.
Example: Construct -24856 in 16-bit two’s complement.
Simple binary | 0110 0001 0001 1000

## Slide 13: Signed Integer Representations
Constructing a negative number in two’s complement
  Form the simple binary (positive) representation of the number.
  Flip all the bits (exchange 0’s for 1’s and 1’s for 0’s)
  Add 1 to the resulting number.
Example: Construct -24856 in 16-bit two’s complement.
Simple binary | 0110 0001 0001 1000
Flip bits | 1001 1110 1101 0111

## Slide 14: Signed Integer Representations
Constructing a negative number in two’s complement
  Form the simple binary (positive) representation of the number.
  Flip all the bits (exchange 0’s for 1’s and 1’s for 0’s)
  Add 1 to the resulting number.
Example: Construct -24856 in 16-bit two’s complement.
Simple binary | 0110 0001 0001 1000
Flip bits | 1001 1110 1101 0111
Add 1 | 1001 1110 1101 1000

## Slide 15: Signed Integer Representations
Summary
  Computers use positional arithmetic.
  Choices in representing negative numbers include signed magnitude, binary coded decimal, and two’s complement.
  Two’s complement solves several problems:
    No “negative zero” representation
    Subtraction becomes addition of a negative number, simplifying CPU hardware.