## Slide 1: Memory Operation

## Slide 2: Memory Operation
Recall detailed architecture

## Slide 3: Memory Operation
Recall detailed architecture
How is memory accessed?

## Slide 4: Memory Operation
MAR and MDR

## Slide 5: Memory Operation
MAR and MDR
n-bit address
n to 2n decoder
CS signal selects a single line
R/W signal 1 for read, 0 for write

## Slide 6: Memory Operation
MAR and MDR
Width of the MAR determines the number of addressable lines. 32-bit machine = 232 ≈ 4 billion addresses.
Width of the MDR determines the word size.
word size × addresses = total memory size

## Slide 7: Memory Operation
Summary
  MAR determines which line of memory to access.
  CS signal activates memory.
  R/W signal selects either to read (1) or write (0) memory.
  MDR sends (write) or receives (read) data to and from memory.

## Slide 8: References
  Englander, I. (2009). The architecture of computer hardware and systems software: an information technology approach. Wiley.