## Slide 1
*
Chapter 1
Data Communications and
Network Management Overview
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 2
*
  Notes
Objectives
Telecommunications overview
Data communications overview
Evolution of converged networks
Desktop processors and LAN technology
Client-Server architecture in networking
Internet and intranet
Network communication protocols
OSI and Internet standards
Broadband networks and services
Need for network management and NMS
Operations, Administration, Maintenance, and Provisioning
Network management architecture and organization
Concept of Network Operations Center
Perspectives of network management
Network management system
Look-ahead of network management technology
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 3
*
  Notes
Telephone Network
Modern network evolution from Telephone / Telecommunications Network
Characteristics of Telephone network
  Reliable - does what is expected of it
  Dependable - always there when you need it (remember 911?)
  Good quality (connection) - hearing each other well
Reasons for QoS:
  Good planning, design, and implementation
  Good operation and management of network
  Migration to new technologies –
    e.g., From analog to digital technology
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 4
*
  Notes
Telephone Network Model
Notice the hierarchy of switches
Primary and secondary routes programmed
Automatic routing
Where is the most likely failure?
Use of Operations Systems to ensure QoS
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 5
*
  Notes
OSSs / NOC
Operations Support Systems (OSSs) help manage the operation of networks
OSSs in telecommunications monitor:
  Analog network parameters:
    S/N ratio, transmission loss, call blockage, etc.
  Digital network parameters:
    Packet loss, Packet delay, Throughput, QoS, etc.
Real-time management of network
Trunk (logical entity between switches / nodes) maintenance system measures loss and S/N Trunks not meeting QoS removed before customer notices poor quality
Traffic measurement systems measure call drops and blockage. Additional switches or routers planned to keep the call blockage or drops below acceptable level
OSSs distributed at central offices and customer premises
Network management done centrally from Network Operations Center (NOC)
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 6
*
  Notes
Data and Telecommunication Network
Computer data is carried over long distance by telephone (telecommunication network)
Output of telephone is analog and output of computers is digital
Modem is used to “modulate” and “demodulate” computer data to analog format and back
Clear distinction between the two networks is getting fuzzier with modern multimedia networks
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 7
*
  Notes
Migration to Digital Technology
Analog transmission migrated to digital transmission
Analog sources converted to digital signals
CPE (Customer Premises equipment) included digital PBX (Private Branch Exchanges)
Analog bandwidth hierarchy migrated to synchronous digital hierarchy
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 8
*
  Notes
DCE with LAN
DCE.. Distributed Computing Environment
Driving technologies for DCE:
  Desktop processor
  LAN
  LAN - WAN network
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 9
*
  Notes
LAN-WAN Network
Major impacts of DCE:
  No more monopolistic service provider
  No centralized IT controller
  Hosts doing specialized function
  Client/Server architecture formed the core of DCE network
Figure 1.5(b) Remote LANs Interconnected by WAN
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 10
*
  Notes
Client/Server Model
Post office analogy; clerk the server, and the customer the client
Client always initiates requests
Server always responds
Notice that control is handed over to the receiving entity.
Request
Response
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 11
*
  Notes
Client/Server Examples
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 12
*
  Notes
TCP/IP Based Networks
TCP/IP is a suite of protocols
Internet is based on TCP/IP
IP is Internet protocol at the network layer level
TCP is connection-oriented transport protocol and ensures end-to-end connection
UDP is connectionless transport protocol and provides datagram service
Internet email and much of the network mgmt. messages are based on UDP/IP
ICMP part of TCP/IP suite
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 13
*
  Notes
Internet Configuration
Walk through the scenario of email from Joe to Sally
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 14
*
  Notes
Architecture, Protocols and Standards
Communication architecture
  Modeling of communication systems, comprising
    Functional components
    Operations interfaces between them
Communication protocols
  Operational procedures
    Intra- and inter-modules
Communication standards
  Agreement between manufacturers on protocols of communication equipment on
    Physical characteristics
    Operational procedures
Examples: (Students to call out)
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 15
*
  Notes
Communication Architecture
Inter-layer interface: user and service provider
Peer-layer protocol interface
Analogy of hearing-impaired student
Role of intermediate systems
Gateway: Router with protocol conversion as gateway to an autonomous network or subnet
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 16
*
  Notes
OSI Reference Model
Importance of the knowledge of layer structure in NM
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 17
*
  Notes
OSI Layers and Services
Importance of services offered by different layers and the protocol conversion at different layers in NM
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 18
*
  Notes
PDU Communication Model
What is the relevance of PDU model in NM?
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 19
*
  Notes
Gateway
cc:mail from a station in Novel IPX network to an Internet station with SMTP email
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 20
*
  Notes
OSI and Internet
Simplicity of Internet; specifies only layers 3 and 4
Integrated application layers over Internet
Commonality of layers 1 and 2 - IEEE standard
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 21
*
  Notes
Application Protocols
Internet user OSI user
Telnet Virtual Terminal
File Transfer Protocol File Transfer Access & Mgmt
Simple Mail Transfer Message-oriented Text Protocol Interchange Standard
Simple Network Common Management Management Protocol Information Protocol
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 22
*
  Notes
Broadband Network
Chapter 1 Data Communications and NM Overview
Figure 1.19 Broadband Network Segments and Technologies
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 23
*
  Notes
Broadband Access Networks
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 24
*
  Notes
Centrally Managed Network Issues
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 25
*
  Notes
Some Common Network Problems
Loss of connectivity
Duplicate IP address
Intermittent problems
Network configuration issues
Non-problems
Performance problems
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 26
*
  Notes
Challenges of IT Managers
Reliability
Non-real time problems
Rapid technological advance
Managing client/server environment
Scalability
Troubleshooting tools and systems
Trouble prediction
Standardization of operations - NMS helps
Centralized management vs. “sneaker-net”
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 27
*
  Notes
Network Management
OAMP
  Operations
  Administration
  Maintenance
  Provisioning
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 28
*
  Notes
NM Functional Flow Chart
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 29
*
  Notes
Dumbbell Architecture
Message exchange between NMSs managing different domains
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 30
*
  Notes
NM Components
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 31
*
  Notes
Interoperability
Message exchange between NMSs managing different domains
Figure 1.26 Network Management Interoperability
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 32
*
  Notes
Network Management Perspectives
Network Management
Service Management
Service and Network Provisioning
Application Management
e-Commerce Management
Inventory Management
Integrated Management
Business Management
Information Management
Management Protocols
Management Technologies
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 33
*
  Notes
Infrastructure Perspective
Domains
Protocols
Technologies
Transmission Media
Transmission Modes
Service Functions
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 34
*
  Notes
Service Perspective
Communication Services
Computing Services
Content Services
IT Services
Application Services
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *

## Slide 35
*
  Notes
Status and Future Trends
Status:
  SNMP management
  Limited CMIP management
  Operations systems
  Polled systems
Current Focus:
  Object-oriented approach
  Service and policy management
  Business management
  Web-based client management
Future Trends
  Web-based management?
  XML based management
Chapter 1 Data Communications and NM Overview
Network Management: Principles and Practice
© Mani Subramanian 2010
Notes: *